| This form has been completed in accordance with the Hazard Management Policy/Procedure and Plant and Equipment Safety Management Policy/Procedure. For further information please refer to the OHS Regulations Part 3 Plant | Overall risk rating (existing controls) highest score eg L, M, H, VH | M |
| --- | --- | --- |
| STEP 1 : ENTER INFORMATION ABOUT THE ITEM OF PLANT/EQUIPMENT, ITS LOCATION AND THE PEOPLE COMPLETING THE RISK ASSESSMENT |
| Plant Location: | HALLAM | Owner of Plant: BIAMA GROVE PTY LTD | SERIAL NO: 43939 HOURS: 1.3 | Date assessed: 29/01/2018 |
| Plant: (Include name and model) | KUBOTA KX018-4 EXCAVATOR | Review date: 29/01/2019 (1 yr, from RISK ASSESSMENT) |
| Purpose of Plant: | CIVIL CONSTRUCTION |
| Current Photo of machine being assessed. | REGISTRATION/LICENCES/ COMPETENCIES (Refer Appendix B) Registration required? Yes No Licence/ Trade certificate required? Yes No Supervisor assessment required? (Induction required for this plant) Yes No Other competency required? Yes No Include in Safe Operating Procedure | LEGISLATION OHS Legislation and/or Australian Standard to be used for further reference. OHS Regulations (2007) Divisions: 1.2 OHS Responsibilities 1.3 Information, Instruction, Training, Induction, Supervision 2.10 Noise Part 3 Plant (including) 3.2.25 Plant with moving parts 3.2.15 Hazard Management 3.2.17 Control of risk AS 4024 - 2006 Safety of machinery AS 1788 Abrasive wheels AS 60204.1 electrical equipment for industrial machines | RISK ASSESSMENT TEAM Operator: HSO/Manager: HSR: Assessor: STEPHEN CADDEN Consultant: COREY HAWORTH Date Assessed: 29/01/2018 STEPHEN CADDEN _____________________ (Signature) (Name) |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can the following items become entangled (eg in moving parts)? |  |
| Yes (e.g. Hair, Jewellery, Clothing, Cleaning aids (cloth), Gloves or Other___________________ No NA | UNLIKELY | FIRST AID | MEDIUM | When in operation, pedestrians to keep clear | El Su En Is Ad PPE | Warning decals in place. Guards are installed. Engine covers are fitted. Induction. | N |  |
| Are emergency stop buttons adequate? |  |
| Yes (within easy reach and clearly marked) No Other issues______________ NA |  |  |  |  | El Su En Is Ad PPE | Customer to organise installation if any additional ones required. | N |  |
| Are there adequate fire extinguishers fitted? |  |
| No |  |  |  |  |  | Customer to organise installation if required | N |  |
| Is there a working travel alarm fitted? |
| Yes. |  |  |  |  |  |  | N |

| Is there a working flashing beacon? |
| --- |
| Yes. |  |  |  |  |  |  | N |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone be crushed by: |  |
| Plant falling or unexpected movement of the plant eg Tipping Falling Rolling over Rolling forward The plant’s load Under/between plant and a structure eg wall Inability to apply brake Falling off the plant Part of the plant collapsing/changing shape Other issues _____________ No NA | UNLIKELY | MAJOR | MEDIUM | Unstable ground. Unexpected movement. Working near structures. Sudden reversing. Operator not wearing seatbelt. Working near pedestrians. Working on plant during maintenance and servicing. | El Su En Is Ad PPE | Neutral start switch fitted. Travel alarm and beacon fitted. Pedals are non-slip. Warning decals fitted. Park brake operational. Control pod operational. ROPS/FOPS structure fitted. Seatbelt fitted. Handrails fitted. SWL decals fitted. Do not lift above personnel decal fitted. Induction. | N |  |
| Can anyone be cut, stabbed or punctured, amputated by coming into contact with : |  |
| Moving plant or parts Sharp or flying objects Work pieces ejected Work pieces disintegrating Other issues______________ No NA | UNLIKELY | MAJOR | MEDIUM | Pedestrians to keep clear 30 metres. Quick hitch failure. Moving blade or bucket. | El Su En Is Ad PPE | Warning decals fitted. Quick hitch safety switch fitted. Induction. | N |  |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone be injured from an electrical shock? |  |
| Water near equipment Plant located near or in contact with exposed live electrical conductors Leads/switch in poor condition Overhead and underground wires Other issues_____________ No NA | UNLIKELY | MAJOR | MEDIUM | Working near high voltage services. Inspecting battery and leads. Digging near underground services. | El Su En Is Ad PPE | Dial Before You Dig decal fitted. Look Up & Live decal fitted. Insulated electrical system. Induction. | N |  |
| Can anyone be injured by an explosion? |  |
| Gas Vapour Dust Liquid Other issues ____________ No NA | UNLIKELY | MAJOR | MEDIUM | When inspecting battery. When filling with fuel | El Su En Is Ad PPE | No smoking around machine. Diesel only decal fitted. Care to be taken when inspecting battery. Induction. | N |  |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone be burnt due to friction? |  |
| Contact with moving parts or surface of the plant Material handled by the plant Other issues _____________ No NA |  |  |  |  | El Su En Is Ad PPE |  | N |  |
| Can anyone be struck by moving objects due to: |
| Plant/materials being ejected Plant/material movement Other issues _____________ No NA | UNLIKELY | MAJOR | MEDIUM | Load may shift, pedestrians to keep clear 30 metres. Unexpected plant movement | El Su En Is Ad PPE | Travel alarm and beacon fitted. Keep clear decals fitted. Swing area decals fitted. Induction for correct operation. ROPS/FOPS structure fitted. | N |  |
| Can anyone suffocate due to: |  |
| Lack of oxygen Atmospheric contamination Engulfment Other issues _____________ No NA | RARE | MAJOR | MEDIUM | When working in confined spaces operator may be overcome by exhaust fumes. | El Su En Is Ad PPE | Training for confined spaces must be completed before undertaking this type of work. Induction. | N |  |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone be burnt due to: |  |
| High/low temperature Naked flame Steam Laser beams Other issues _____________ No NA | UNLIKELY | FIRST AID | MEDIUM | When inspecting radiator. On exhaust. | El Su En Is Ad PPE | Hot coolant decal fitted. Hot exhaust decal fitted. Exhaust located out of reach of operating position, and all pedestrians to keep clear. | N |  |
| Can anyone be affected by temperature extremes? |  |
| Exposure to high temperature Exposure to low temperature Other issues _____________ No NA | RARE | FIRST AID | LOW | When working in extremes of temperature. | El Su En Is Ad PPE | Sunscreen to be worn. Appropriate clothing to be worn. Induction and training. | N |  |
| Can anyone slip, trip or fall due to: |  |
| The location of the plant Uneven work surfaces Lack of safe guards (eg rails) Slippery work surfaces Other issues _____________ No NA | POSSIBLE | FIRST AID | MEDIUM | When working on uneven ground. When entering and exiting plant. | El Su En Is Ad PPE | Seatbelts must be worn at all times. Maintain 3 points of contact when entering or exiting machine. Handrails fitted. Safety decals fitted. Steps to be kept clean. | N |  |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone come into contact with fluids or gases under high pressure due to: |  |
| Failure of the plant Nature of the plant Other issues _____________ No NA | UNLIKELY | MAJOR | MEDIUM | Hydraulic hoses may burst. Radiator hoses may burst. | El Su En Is Ad PPE | High pressure fluid decals fitted. Hose clamps fitted. Hose covers fitted. Hoses in good condition and correct maintenance to be continued. | N |  |
| Can anyone injured due to ergonomic issues due to: |  |
| Repetitive body movement or posture Insufficient space Excessive effort (push/pull) Working at a height Seating design Poor lighting Other issues _____________ No NA | POSSIBLE | FIRST AID | MEDIUM | Long periods of operation | El Su En Is Ad PPE | Ergonomic and adjustable seat fitted. Low stress controls fitted. Good lighting fitted. Control knobs easy to reach. Operator to take correct break periods. | N |  |
| Is there a current operators manual? |  |
| Yes |  |  |  |  |  |  | N |  |

| LEGEND El = Elimination Su = Substitution En = Engineering | Is = Isolation Ad = Administration PPE = Personal Protective Equipment |  |
| --- | --- | --- |

| Hazard Identified | Likelihood | Consequence | Score | Comments (ie when and where hazard is present, task/activity) | Hierarchy of control | Current Controls | Action required Y/N |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Can anyone be injured or suffer ill health from exposure to other hazards? |  |
| Chemicals Radiation Fumes Dusts Vibration Noise Toxic gases or vapours Other issues _____________ No NA | UNLIKELY | MAJOR | MEDIUM | Working in confined spaces. Long periods of operation | El Su En Is Ad PPE | No excessive fumes at high idle. Falls below 85Db limit. Hearing protection decal fitted. Operator to be trained in correct safety procedure for dusty work environments. | N |  |
| Does the plant generate significant environmental hazards |  |
| Energy consumption Water consumption Hazardous waste Hazardous emissions Nuisance noise Produce ignition to the surrounding area Other issues _____________ No NA |  |  |  |  | El Su En Is Ad PPE | Fitted with emissions compliant engine. Noise level below 85Db limit. | N |  |

# STEP 3 : ACTION REQUIRED BY MANAGER/SUPERVISOR/AUTHORISED PERSON

If no actions required and residual risk is medium to very high, the activity and the hazard(s) have been transferred to the Hazard Register and communicated to the relevant personnel.

______________________________________________________________________________________________________________________

_PLEASE NOTE:       ________________________________________________________________________________________________________________

_________________HALF HITCH FITTED SAFTY PIN MUST BE FITTED BEFORE USE

_____________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________

# RISK ASSESSMENT TABLES

# Likelihood Table

| CATEGORY | DESCRIPTION |
| --- | --- |
| Almost Certain | Incident will occur at some time (0 – 1 month) |
| Likely | Incident could occur at some time (1 month – 1 year) |
| Possible | Incident is possible to occur (1 year – 2 years) |
| Unlikely | Incident is possible, but unlikely to occur (2 years – 5 years) |
| Rare | Cannot imagine that this could occur (over 5 years) |

# Consequences Table

| CATEGORY | DESCRIPTION |
| --- | --- |
| Minor | Effects unlikely to last until the next day. |
| First Aid | Likely to affect employee the next day. |
| Major | Medical Treatment injury needs formal medical treatment |
| Critical | Injury requiring extensive medical treatment and/or hospitalization |
| Catastrophic | Injury resulting in death or permanent incapacity |

# Risk Score Calculator

| Likelihood | Consequences |
| --- | --- |
|  | Minor | First Aid | Major | Critical | Catastrophic |
| Almost certain | Medium | High | High | Very High | Very High |
| Likely | Medium | Medium | High | High | Very High |
| Possible | Low | Medium | High | High | High |
| Unlikely | Low | Low | Medium | Medium | High |
| Rare | Low | Low | Medium | Medium | High |

# Risk Priority Table

| Descriptor | Priority | Action |
| --- | --- | --- |
| Very High | 1 | Immediate action required. The activity should cease immediately and short term safety controls implemented. Notify Manager and assess activity. |
| High | 2 | Implement short term safety controls immediately. Notify Manager and assess activity |
| Medium | 3 | Short term safety controls implemented to minimise risk of injury. Notify Manager and assess activity. Corrective Actions within one month. |
| Low | 4 | Notify Manager and assess activity. Corrective Actions within three months (if possible). |

# Text boxes

Safety around operating plant

Machines have blind spots where operators may not see people or objects nearby.

The following diagrams illustrate typical examples of blind spots for some common mobile plant.